## Slide 1: Real-Time Abiotic Monitoring in the Hudson
Brittney Flaten
NEIWPCC & NYSDEC
October 8, 2024

## Slide 2: Acknowledgements

## Slide 3: What do we mean when we say “abiotic”?
Non-living components of the ecosystem
In the River:
  Temperature
  Salinity
  Turbidity
  Substrate composition
  Water velocity

## Slide 4
Who cares?

## Slide 5: A Brief and Incomplete History of Abiotic Monitoring
Mid-90s: Monitoring at HRNERR
  System-wide Monitoring Program
2008: Established network of sites from Schodack to Castle Point
  Hudson River Environmental Conditions Observing System
Goal: Provide widespread, high frequency data
Notes: Sawkill, Stony Creek, Tivoli Bays
Emphasize importance of high frequency data

## Slide 6
Hudson River Environmental Conditions Observing System (HRECOS)
Network of water quality monitoring stations
  Plus weather stations
Data recorded every 15 minutes
Transmitted online every hour
  “Near real-time”
Parameters include:
  Water temperature
  Dissolved oxygen
  Conductivity
  Turbidity
  pH
  Chlorophyll & phycocyanin at select sites
Anyone can access it!

## Slide 7: What goes into real-time monitoring?

## Slide 8
Multiparameter sondes
Sensors
Calibration

## Slide 9
Deployment tube
Enclosure
A look inside…

## Slide 10
Wildlife conflicts
Plant interference
Aquatic life

## Slide 11
Data ultimately end up on web service or an API
????

## Slide 12
Source: USGS Water Data

## Slide 13
Source: CDMO Real-Time Application

## Slide 14
Source: Hudson River Park

## Slide 15
What if I want to download the data?

## Slide 16: So Many Choices!
USGS Water Data
USGS Mapping Application
NERRS Centralized Data Management Office
dataRetrieval in R

## Slide 18: What can we learn?

## Slide 20
Notes: 11 stations

## Slide 28
Questions?
Brittney.Flaten@dec.ny.gov
hrecos@dec.ny.gov
hrecos.org