## Slide 1
Sounding the Hudson: Applications of Bioacoustics for Ecosystem Monitoring in the Hudson River
Rebecca E. Cohen1, Patrick Baker2, Christopher Bowser3,4,5, Matthew Breece6, Alexander S. Flecker7, Dewayne Fox8, Amanda Higgs4,5, Maija Niemistö3,4,5, Richard Pendleton4,5, Suresh A. Sethi9, Shannon White10, Aaron N. Rice1
1 K. Lisa Yang Center for Conservation Bioacoustics, Cornell Lab of Ornithology, Cornell University
2 United States Military Academy
3 Hudson River National Estuarine Research Reserve
4 New York State Department of Environmental Conservation
5 Cornell Water Resources Institute
6Marine Science Department, St. Mary’s College of Maryland
7 Department of Ecology & Evolutionary Biology, Cornell University
8 Department of Agriculture & Natural Resources, Delaware State University
9 Department of Earth & Environmental Sciences, CUNY Brooklyn College
10United States Geological Survey

## Slide 2
Background
Goals:
Understand how key fish species use Hudson River and HRNERR component site habitats
Monitor protected species in a cost-effective manner while minimizing harm, physical stress, or behavioral response
Foster public engagement and stewardship via science outreach and education tools
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Funded by NOAA-NERRS to explore applications of bioacoustics for protected fish species & ecosystem monitoring in the Hudson
2 smaller spinoff projects funded by WRI
Species of interest
Why bioacoustics?
Marine background
Sound vs light
Non-invasive

## Slide 3
Entails collection of soundscape data to identify presence of species of interest
Active sound production documented in ~1000 fish species (Looby et al. 2022)
  96% of species still uncharacterized
Sound production likely to be widespread in actinopterygian fish (Rice et al. 2022)
Passive Acoustic Monitoring (PAM)
Broadband Soundscape Recording
Digitization
Spectrogram Generation
Automated Detection/Classification
Species Acoustic Activity Time Series
Soundscape Metric Computation
Soundscape
Characteristics
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: How bioacoustics?

## Slide 4
Main channel:
SoundTrap ST600
Tributaries/Wetlands: Swift Recorder w cabled hydrophone
Study Sites: HRNERR Component Sites, plus Hyde Park area
SoundTrap
Swift
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Have some pilot data from 2020-2022
Broadscale monitoring across region began April 2023
Last year and this year, recorded at NERRS component sites (plus Hyde Park Atl Stur spawning site) from April-Oct
Additional recording locations for each WRI project
Start w WRI project

## Slide 5
Study Sites: HRNERR Component Sites, plus Hyde Park area
SoundTrap
Swift
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Does not include last leg of data collection this year
Start with a WRI project

## Slide 6
Water Chestnut vs. Submerged Aquatic Vegetation Soundscapes
Acoustic Recorder
Oxygen Sensor
Trapa natans
31 May, 2022
13 July, 2022
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Estuarine habitats are dynamic, substantial fluctuations in temperature, salinity, vegetation, flow speed & direction on seasonal & tidal cycles
Exemplified by invasive water chestnut growth

## Slide 7
Water Chestnut vs. Submerged Aquatic Vegetation Soundscapes
SAV Bed
Water Chestnut
Acoustic Recorder
Oxygen Sensor
Trapa natans
 How does invasive vegetation alter Hudson River soundscapes?
Invasive water chestnut known to alter the physical and chemical habitat
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Know that the chestnut changes physical & chemical habitat, wondered how this affects the soundscape?

## Slide 8
Water Chestnut vs. Submerged Aquatic Vegetation Soundscapes
Trapa natans
Acoustic Recorder
Oxygen Sensor
Sound levels substantially lower in the chestnut bed
Dampened sound propagation? Diminished community? Both?
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Long-term spectral average – spectrogram for long durations of data
Shown here are two weeks
Time on the x, frequency on the y, acoustic power given by color
Overall, much lower sound levels within chestnut bed, as compared to SAV beds
Data from all devices except the Chestnut one looked like the upper plot

## Slide 9
Water Chestnut vs. Submerged Aquatic Vegetation Soundscapes
Trapa natans
Acoustic Recorder
Oxygen Sensor
Sound levels substantially lower in the chestnut bed
Dampened sound propagation? Diminished community? Both?
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Can also view this more simply as broadband power levels at each site versus time
dB is log scale,
Could be attributed to a few different things:
Physical dampening of sound propagation
Tangled mess of roots and leaves throughout water column
Low O2 environment hostile towards native river species, diminished community within chestnut bed
Impacts:
If due to sound propagation conditions – could reduce acoustic communication space, essential ambient cues used to identify optimal habitat
Poor sound propagation could also provide acoustic refugia from acoustics-based predation

## Slide 10
Atlantic Sturgeon
Adapted from Fig. 2, Higgs & Beach (2021)
Data shared by D. Higgs
Amplitude (kU)
Frequency (kHz)
0
-10
-20
10
20
0.5
1
1.5
2
00:30
01:00
01:30
02:00
02:30
Time (mm:ss)
Related Work – Lake Sturgeon Thunder
Acipenser oxyrinchus
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Priority species: Atl Stur
4 of 5 DPS listed as endangered
Many data gaps due to difficulty of observing this highly mobile species, strict regulations on sampling due to protected status
Good candidate for bioacoustics monitoring, based on reports of sound production in closely-related species (mostly lake sturgeon, also pallid & shovelnose, maybe 5 Russian species)
Spawning sounds reported for lake sturgeon, provided starting point
Spectrum, grayscale spectrogram, waveform, color spectrogram

## Slide 11
Atlantic Sturgeon
Acipenser oxyrinchus
Recorder
Location
Atlantic Sturgeon Spawning Aggregation
Adapted from Fig. 2, Higgs & Beach (2021)
Data shared by D. Higgs
Amplitude (kU)
Frequency (kHz)
0
-10
-20
10
20
0.5
1
1.5
2
00:30
01:00
01:30
02:00
02:30
Time (mm:ss)
Related Work – Lake Sturgeon Thunder
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Recorder just south of Poughkeepsie Yacht Club, started with few weeks of recording from 2021
Known site of Atl Stur spawning,
Looked for signals similar to lake sturgeon thunder

## Slide 12
Atlantic Sturgeon
27:32:00
27:32:10
27:32:20
27:32:30
27:32:40
27:32:50
Frequency (kHz)
0.5
1
1.5
2
Time (hh:mm:ss)
New Findings – Atlantic Sturgeon Thunder?
Acipenser oxyrinchus
Adapted from Fig. 2, Higgs & Beach (2021)
Data shared by D. Higgs
Amplitude (kU)
Frequency (kHz)
0
-10
-20
10
20
0.5
1
1.5
2
00:30
01:00
01:30
02:00
02:30
Time (mm:ss)
Related Work – Lake Sturgeon Thunder
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: During period of known Atl stur spawning (based on gill netting, acoustic telemetry tags, egg mats), found similar thunders
Visible on spectrogram (white boxes)
Average waveform and spectrum shown below (w noise spectrum for comparison)
Quite numerous throughout late May & June, not present earlier in the spring or later in the summer

## Slide 13
Atlantic Sturgeon
No Strong Diel Periodicity
Thunder Occurrence Well-correlated with Presence of Telemetry Tagged Sturgeon
Acipenser oxyrinchus
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: No consistent diel pattern in sound production
Top left – date on y, hour of day on x, shaded regions show nighttime, blue shows presence of thunders in 1-min bins
Very episodic in occurrence
Collapsed across all days of the 2021 data collection period, histogram below shows counts of calls in each hour of the day
Slightly higher occurrence of calls in hours prior to and just after dawn, but again, not consistent across the recording period
Daily presence tightly correlated with presence of telemetry-tagged fish at nearest receiver (1.8km north; 26 tagged individuals detected during this time; max of 18 on any given day)
Going to look into correlation btwn thunder occurrence & demographics, though sample size is small
This summer, recorded at Bears Bluff; one spawning event in our tank
Waiting to see that data to hopefully provide validation of this sound-species assignment

## Slide 14
27:32:00
27:32:10
27:32:20
27:32:30
27:32:40
27:32:50
Frequency (kHz)
0.5
1
1.5
2
Time (hh:mm:ss)
Freshwater Drum
Aplodinotus grunniens
Continuous band of sound energy from many simultaneously-calling Freshwater Drum
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: May have noticed another strong signal in the spectrogram with the putative Atlantic Sturgeon thunder
Known signal – chorusing of Freshwater Drum
Family Sciaenidae, many species commonly called Drums or Croakers

## Slide 15
27:32:00
27:32:10
27:32:20
27:32:30
27:32:40
27:32:50
Frequency (kHz)
0.5
1
1.5
2
Time (hh:mm:ss)
Freshwater Drum
Aplodinotus grunniens
Chorusing events dominate the soundscape for hours each day
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Chorusing is a daily event during spawning season (mid-May – Aug)
One week of data shown on LTSA to the right, daily drum chorus evident in the 200-400 Hz band
Non-native in the Hudson River, thought to have entered via NYS canal system in the 80’s
Extent of colonization not well characterized
Wanted to look at drum presence across our sites, which span ~100 mi (river mile 25 – 125)
Rodney Rountree & Francis Juanes observed that freshwater drum are likely the “dominant biological contributors to the underwater soundscape throughout their range, with few other organisms producing sounds of similar magnitude of the drum chorus”

## Slide 16
Freshwater Drum
Stockport
Tivoli
Hyde Park
Iona
Piermont
Aplodinotus grunniens
0
2
4
0
2
4
0
2
4
0
2
4
0
2
4
16 Jun
17 Jun
18 Jun
19 Jun
20 Jun
21 Jun
Frequency (kHz)
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: LTSAs from each river channel site for 6/15-6/21 period
Very different noise conditions across sites
Drum really dominate at Hyde Park (Atl Stur spawning site)
Surprisingly, still chorusing as far south as Piermont, which is typically below the salt front
Low levels of acoustic activity at Iona, not hearing them at all at Stockport
Next steps are to look at relationship between drum chorusing and environmental factors (e.g. salinity, depth, water temp, substrate)

## Slide 17
Shortnose Sturgeon
Acipenser brevirostrum
Lots of funny sounds, no strong ID (yet!)
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Share un-ID’d weird plinky sounds

## Slide 18
Shortnose Sturgeon
Acipenser brevirostrum
Lots of funny sounds, no strong ID (yet!)
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Share un-ID’d weird plinky sounds

## Slide 19
Shortnose Sturgeon
Acipenser brevirostrum
Lots of funny sounds, no strong ID (yet!)
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Share un-ID’d weird plinky sounds

## Slide 20
River Herring
Alosa pseudoharengus
Alosa aestivalis
Weir deployed in Black Creek in 2020 & 2021
Damaged by high flow events in 2022 & 2023, not deployed in 2024
Very little acoustic data overlap
No sounds yet, stay tuned..
Hourly weir Counts
2021
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu
Notes: Cite Staples 2022 herring splash paper
Challenges of identifying new sounds
Current work w GoPro footage in Black Creek

## Slide 21
In Progress:
Atlantic Sturgeon thunder occurrence/phenology across sites
Hudson river soundscapes
Across salinity gradient
Main channel vs tributaries/wetlands
Atlantic Sturgeon & Freshwater Drum sound mapping
Ongoing Analysis
500m
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu

## Slide 22
Acknowledgements
Many thanks to:
Norrie Point Environmental Center
Dan Miller (NYSDEC, HRNERR)
Dennis Higgs (University of Windsor)
Ella Agoos (Norrie Point)
Nicholas Pauley (West Point)
Contact:
Rebecca Cohen
r.cohen@cornell.edu
https://www.birds.cornell.edu/ccb/rebecca-cohen-ph-d/
Funding Sources:
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
www.bioacoustics.cornell.edu

## Slide 23
Hudson River Symposium, 8 October 2024, Cary Institute for Ecosystem Studies
Water Chestnut vs. Submerged Aquatic Vegetation Soundscapes
www.bioacoustics.cornell.edu
Notes: Sensitivity highly variable across frequencies and Hydromoths, but water chestnut device not noticeably lower sensitivity across the board than the others